## Slide 1
M.Tech Program
Advanced Industry Integrated Programs
Jointly offered by University and LTIMindTree
Review II
Project Title
Risk- and Cost-Aware AI Maintenance Decision Engine for Industrial Power Assets Using Vibration-Based Fault Diagnosis
Team Member
SUBASH M | T9970
RAJALAKSHMI ENGINEERING COLLEGE
Knowledge partner | Implementation partner

## Slide 2
Unplanned failures of motors, pumps and generators cause downtime, safety hazards and high repair costs; bearing faults are a leading cause.
Vibration signals carry fault signatures that AI can classify as Normal, Ball, Inner-Race or Outer-Race faults.
Review I established the problem, the literature gap and the five-module plan.
Review II presents the methodology, data preprocessing & EDA, algorithms and tools, milestone progress and the end-to-end pipeline.
Core idea: link diagnosis → risk → cost → action in one framework that recommends Monitor, Inspect or Repair.
Introduction
Risk- and Cost-Aware AI Maintenance Decision Engine

## Slide 3
Build a 1D-CNN classifier for Normal, Ball, Inner-Race and Outer-Race faults from raw vibration segments.
Benchmark it against classical ML trained on handcrafted time- and frequency-domain features.
Evaluate C-GAN synthetic signals for class balancing and data augmentation.
Compute a dynamic risk score from fault probability, severity, asset criticality and operating stress.
Select the minimum expected-cost action (Monitor, Inspect or Repair).
Deliver the full workflow through an interactive Streamlit dashboard.
Objective
Risk- and Cost-Aware AI Maintenance Decision Engine

## Slide 4
Data Acquisition
CWRU Bearing Dataset: drive-end accelerometer signals sampled at 12 kHz under motor loads of 0–3 HP.
Fault diameters of 0.007", 0.014" and 0.021" for Ball, Inner-Race and Outer-Race faults, plus Normal baseline.
Segmentation & Labelling
Signals split into fixed-length sliding windows with overlap to increase training samples.
Each window z-score normalised and labelled with one of the 4 classes.
Stratified train / validation / test split, separated by recording to prevent data leakage.
Module 1 – Data Preprocessing & Signal Segmentation
Risk- and Cost-Aware AI Maintenance Decision Engine

## Slide 5
Model Design
Stacked Conv1D → BatchNorm → ReLU → MaxPool blocks learn fault patterns directly from raw signals.
Global average pooling and a softmax layer output the probability of each fault class.
Training & Evaluation
Adam optimiser, cross-entropy loss and early stopping on validation loss.
Metrics: accuracy, macro-F1 and confusion matrix; robustness tested across motor loads.
Baseline: Random Forest / SVM on RMS, kurtosis, crest factor and FFT band energies.
Module 2 – Bearing Fault Diagnosis (1D-CNN)
Risk- and Cost-Aware AI Maintenance Decision Engine

## Slide 6
Generator & Discriminator
Class-conditioned 1D generator produces vibration segments for a chosen fault type.
Discriminator learns to separate real from synthetic signals for each class.
Quality & Augmentation Study
Synthetic signals compared with real ones using FFT spectra and statistical features.
Classifier trained with vs without augmentation to measure the effect on minority fault classes.
Module 3 – C-GAN Synthetic Vibration Data Generation
Risk- and Cost-Aware AI Maintenance Decision Engine

## Slide 7
Risk Factors
Fault probability (P) from the 1D-CNN softmax output.
Severity (Sev) weighted by fault type and fault size.
Asset criticality (C) and operating stress (S) from load and speed conditions.
Risk Scoring
Risk = P × Sev × C × S, normalised to a 0–1 scale.
Mapped to Low / Medium / High bands and recomputed for every new signal window (dynamic).
Module 4 – Dynamic Risk Assessment
Risk- and Cost-Aware AI Maintenance Decision Engine

## Slide 8
Cost-Aware Decision
Expected cost of each action = action cost + residual failure probability × failure cost.
Failure cost covers downtime, repair and secondary damage.
The action with the lowest expected cost is recommended: Monitor, Inspect or Repair.
Streamlit Dashboard
Upload a signal → view predicted fault & confidence, risk gauge, cost comparison and the recommended action with its rationale.
Module 5 – Cost-Aware Decision Engine & Dashboard
Risk- and Cost-Aware AI Maintenance Decision Engine

## Slide 9
Methodology / Modeling Plan
Risk- and Cost-Aware AI Maintenance Decision Engine
1
Data Preparation
Load CWRU signals
Window, normalise, label
Stratified split
2
Fault Diagnosis
Baseline ML on features
1D-CNN on raw signals
Compare F1 & accuracy
3
Data Augmentation
Train class-conditioned C-GAN
Validate synthetic quality
Retrain with augmentation
4
Risk Scoring
Fuse P, severity, criticality, stress
Low / Medium / High bands
5
Decision & Deployment
Expected-cost per action
Recommend best action
Streamlit dashboard
Modeling plan: baseline ML → 1D-CNN → CNN + C-GAN augmentation, compared on accuracy, macro-F1 and robustness across motor loads; best model feeds the risk and cost engine.

## Slide 10
Data Preprocessing & EDA
Risk- and Cost-Aware AI Maintenance Decision Engine
Data Preprocessing
Load .mat files and extract the drive-end (DE) channel.
Sliding-window segmentation into fixed-length samples.
Z-score normalisation per segment.
Label encoding into 4 classes.
Stratified split by recording to avoid leakage.
Class-balance check across fault types and loads.
Exploratory Data Analysis
Time-domain waveforms per class – fault classes show periodic impulses.
Statistical features (RMS, kurtosis, crest factor) compared across classes.
FFT & envelope spectra inspected near bearing defect frequencies (BPFI, BPFO, BSF).
Class distribution reviewed – imbalance motivates C-GAN augmentation.
Load-wise comparison of signals from 0–3 HP.

## Slide 11
Approach / Algorithms / Tools
Risk- and Cost-Aware AI Maintenance Decision Engine
Component | Algorithm / Technique | Tools
Signal processing | Windowing, FFT, envelope analysis | NumPy, SciPy
Baseline classifier | Random Forest / SVM on handcrafted features | Scikit-learn
Fault diagnosis | 1D Convolutional Neural Network | PyTorch
Synthetic data | Conditional GAN (C-GAN) | PyTorch
Risk engine | Weighted risk score: P × Sev × C × S | Python
Cost decision engine | Expected-cost minimisation | Python
Dashboard | Interactive decision support UI | Streamlit, Plotly
Deployment | Version control & containerisation | Git, Docker

## Slide 12
Project Plan / Milestones Progress
Risk- and Cost-Aware AI Maintenance Decision Engine
Phase | Milestone | Status
Phase 1 | Problem definition, literature review, module plan | Completed (Review I)
Phase 2 | CWRU data collection, preprocessing & segmentation | Completed
Phase 3 | Exploratory data analysis & feature study | Completed
Phase 4 | Baseline ML and 1D-CNN fault diagnosis | In progress
Phase 5 | C-GAN synthetic data & augmentation study | In progress
Phase 6 | Risk assessment & cost-aware decision engine | Planned
Phase 7 | Streamlit dashboard, integration & testing | Planned
Phase 8 | Final evaluation, report & paper | Planned (Review III)

## Slide 13
Pipeline Structure
Risk- and Cost-Aware AI Maintenance Decision Engine
CWRU Vibration Data
Drive-end signals, 4 classes
Preprocessing
Windowing, normalisation, split
1D-CNN Classifier
Fault type diagnosis
Fault Output
Class + probability (P)
Risk Engine
P × Severity × Criticality × Stress
Cost Engine
Expected cost per action
Decision
Monitor / Inspect / Repair
Streamlit Dashboard
Fault, risk, cost, action
C-GAN synthetic data → augmentation

## Slide 14
M.Tech Program
Advanced Industry Integrated Programs
Jointly offered by University and LTIMindTree
Review II
Project Title
SafeZone: A Real-Time Worker-Machinery Proximity Alert System for Construction Sites Using YOLO and Perspective-Corrected Distance Estimation
Team Member
SUBASH M | T9970
RAJALAKSHMI ENGINEERING COLLEGE
Knowledge partner | Implementation partner

## Slide 15
Struck-by contact with excavators, loaders and trucks injures workers because operators have blind spots around the machine.
Supervisors cannot watch every camera; close calls go unseen and are rarely recorded.
Review I defined the gap: camera systems measure distance in pixels, which perspective distorts.
Review II presents the methodology, preprocessing & EDA, algorithms and tools, progress and pipeline.
The system combines YOLO11n detection, ByteTrack tracking, homography ground mapping and time-to-contact with Streamlit alerts.
Introduction
SafeZone Proximity Alert System

## Slide 16
Detect workers and machines in site video with a fine-tuned YOLO11n detector.
Track each object across frames with ByteTrack stable IDs.
Map image positions to ground coordinates in metres with a homography.
Estimate distance, machine motion and time-to-contact for every pair.
Raise Safe / Warning / Danger alerts and log near-misses.
Show results in a Streamlit dashboard with analytics and reports.
Objective
SafeZone Proximity Alert System

## Slide 17
Datasets
Use the Construction Site Safety Image Dataset (2,801 images, YOLO format).
Plan MOCS (41,668 images, 13 classes) for machine-type labels.
Detector Training
Fine-tune YOLO11n from COCO weights on a Kaggle T4 GPU at 640 px.
Map classes to worker and machine types (Person, machinery, vehicle).
Export to OpenVINO for CPU inference on the laptop.
Module 1 – Data Preparation & Detector Training
SafeZone Proximity Alert System

## Slide 18
Multi-Object Tracking
ByteTrack: stable IDs for each worker and machine across frames.
Track history: 1.5 s of ground positions per ID.
Smoothing: exponential averaging of box positions to cut jitter.
Homography Calibration
Point pairs clicked on the image with known ground positions.
Homography H (OpenCV findHomography) maps pixels to metres.
Checked with reprojection error in metres.
Module 2 – Tracking & Ground-Plane Mapping
SafeZone Proximity Alert System

## Slide 19
Ground Distance
Worker reduced to a foot point (bottom-centre of the box).
Machine footprint built from the box bottom edge plus machine depth.
Distance
Measure the foot point to footprint distance in metres.
Machine motion from footprint speed and box-shape change.
Compare homography vs pixel distance in the ablation.
Module 3 – Distance & Motion Estimation
SafeZone Proximity Alert System

## Slide 20
Time-to-Contact
Estimate closing speed from the slope of pair distance over 1.5 s.
Compute TTC = distance / closing speed for each worker-machine pair.
Alert Rules
Danger below 5 m or TTC 2 s; Warning below 10 m or TTC 5 s (moving machine).
Label every worker Safe, Warning or Danger on each frame.
Keep all thresholds editable on the Settings page.
Module 4 – Time-to-Contact & Alert Rules
SafeZone Proximity Alert System

## Slide 21
Near-Miss Logging
Each Warning or Danger period stored as one event in SQLite.
Closest distance, lowest TTC and machine state saved per event.
Streamlit Dashboard
Live monitor with danger zones, alert banner and ground-plane map.
Pages for calibration, event log, analytics and settings.
Includes PDF safety reports and an alarm on Danger.
Module 5 – Event Logging & Dashboard
SafeZone Proximity Alert System

## Slide 22
Methodology / Modeling Plan
SafeZone Proximity Alert System
1
Detection
Train YOLO11n
OpenVINO export
Worker / machine boxes
2
Tracking
ByteTrack IDs
Box smoothing
1.5 s track history
3
Ground Mapping
4-point calibration
Homography H
Pixels to metres
4
Risk Engine
Footprint distance
Motion state + TTC
Safe / Warning / Danger
5
Alerts & Dashboard
Near-miss log
Banner + alarm
Streamlit dashboard
Modeling plan: COCO-pretrained YOLO11n → fine-tuned on construction images → homography distance → TTC alerts; evaluated on mAP@0.5, alert precision / recall, lead time and FPS.

## Slide 23
Data Preprocessing & EDA
SafeZone Proximity Alert System
Data Preprocessing
COCO to YOLO conversion of box labels (MOCS) with class merging.
Class mapping of dataset names to worker and machine types.
Train / validation split kept as provided by the dataset.
Letterbox resizing to 640 px for training and inference.
Augmentation (mosaic, HSV, flips) applied by Ultralytics during training.
Exploratory Data Analysis
Class distribution of workers vs machines in the training set.
Box size distribution to check small, distant workers.
Visual label check of sample images before training.
Scene conditions (lighting, camera height, crowding) reviewed.
Calibration check of the 5 m ground grid on test frames.

## Slide 24
Approach / Algorithms / Tools
SafeZone Proximity Alert System
Component | Algorithm / Technique | Tools
Detection | YOLO11n fine-tuned on construction images | Ultralytics, PyTorch
Tracking | ByteTrack multi-object tracking | Ultralytics, lap
Ground mapping | Homography from 4+ point pairs | OpenCV
Risk engine | Footprint distance, motion vote, TTC | NumPy
CPU inference | Model export for Intel CPUs | OpenVINO
Event storage | Near-miss episodes with snapshots | SQLite, Pandas
Training | GPU training in a cloud notebook | Kaggle (T4 GPU)
Dashboard | Live monitor, analytics, PDF report | Streamlit, Plotly

## Slide 25
Project Plan / Milestones Progress
SafeZone Proximity Alert System
Phase | Milestone | Status
Phase 1 | Problem definition, literature review, module plan | Completed (Review I)
Phase 2 | Dataset preparation & YOLO11n detector training | Completed
Phase 3 | Dataset EDA & homography calibration module | Completed
Phase 4 | ByteTrack tracking & ground distance engine | In progress
Phase 5 | Time-to-contact & alert rules | In progress
Phase 6 | Event logging & Streamlit dashboard | Planned
Phase 7 | Real-video evaluation & ablation study | Planned
Phase 8 | Final evaluation, report & paper | Planned (Review III)

## Slide 26
Pipeline Structure
SafeZone Proximity Alert System
Site Video
CCTV, RTSP or video file
Detection
YOLO11n worker / machine boxes
Tracking
ByteTrack IDs + history
Ground Mapping
Homography: pixels to metres
Risk Engine
Distance, motion state, TTC
Alert Levels
Safe / Warning / Danger
Event Log
Near-misses + snapshots
Streamlit Dashboard
Live view, analytics, reports
Flow: video → detection → tracking → ground distance → TTC and alert level → near-miss log → dashboard.